## Slide 1: Chapter 15
Wireless LANs

## Slide 2: Introduction
Differences between wired and wireless LANs
  Medium
    Modern Ethernet LANs use full-duplex (send and receive at the same time) point-to-point communication media
    Wireless LANs use air, usually multiple access broadcast communication (half-duplex)
    Due to low power, devices can only send or receive at a time: half-duplex
  Hosts
    Hosts attached to an Ethernet LAN are effectively fixed
      Moving a host to another network requires a new network address
    Hosts attached to a Wireless LAN usually expect mobility without changing address
      Consider making a call over a data service (Skype, WhatsApp call, etc.) whilst on a train
        Couldn’t do this with Ethernet!

## Slide 3: Introduction
Differences between wired and wireless LANs
  Isolated LANs
    Isolated Ethernet LANs require central link-layer switch
    Isolated wireless LANs do not require a central switch
  Connection to Other Networks
    Ethernet/wireless LANs can connect to other networks through a router
    Wireless LAN stations must first connect to an access point that is in turn connected to the router

## Slide 4: Introduction
Characteristics
  Attenuation – signals decrease rapidly because the signal disperses in all directions
  Interference – often receive signals from other senders using the same frequency band
    The frequencies used by WLANs are often used by other wireless devices, e.g., telephone handsets
  Multipath propagation – signal can be reflected back from obstacles such as walls, causing signals to be received at different phases (signal “echos”)
  Error control – above factors mean error control more serious than for wired network

## Slide 5: IEEE 802.11 Project
IEEE 802.11 defines the physical and data-link layers for wireless LANs (WLANs)
  Sometimes called Wireless Ethernet or WiFi
  Defines two kinds of services:
    Basic Service Set (BSS) – either ad hoc or using a central base station (access point, AP)
      When BSS has an AP, known as infrastructure BSS
    Ad hoc can form a network without an AP but cannot send data to other BSSs, stations agree to be part of a BSS and can locate one another
    Extended Service Set (ESS) – two or more BSS connected through a distribution system
      ESS: distribution system connects the APs in BSSs, communication outside own BSS must be through AP,
      ESS: inside BSS, stations can communicate without AP within range

## Slide 6: IEEE 802.11 Project
IEEE 802.11 defines the physical and data link layers for wireless LANs (WLANs)
  Defines three kinds of stations connected to the WLAN:
    No-transition
      Station is either stationary or mobile within the same BSS
    BSS-transition
      Station can move between BSSs within the same ESS
    ESS-transition
      Station can move between ESSs
      Communication may not be continuous when moving between ESSs

## Slide 7
Figure 15.9: Frame format

## Slide 8
Table 15.1: Subfields in FC field
15.8
Frame control (FC). The FC field is 2 bytes long and defines the type of frame
and some control information.

## Slide 9
D. This field defines the duration of the transmission that is used to set the value of NAV. Network allocation vector (NAV) that shows how much time must pass before stations are allowed to check the channel for idleness.
Addresses. There are four address fields, each 6 bytes long. The meaning of each
address field depends on the value of the To DS and From DS subfields and will be
discussed later.
Sequence control. This field, often called the SC field, defines a 16-bit value. The
first four bits define the fragment number; the last 12 bits define the sequence
number, which is the same in all fragments.
Frame body. This field, which can be between 0 and 2312 bytes, contains information based on the type and the subtype defined in the FC field.
FCS. The FCS field is 4 bytes long and contains a CRC-32 error-detection sequence.
Figure 15.9: Frame format

## Slide 10
Figure 15.10: Control frames

## Slide 11
Figure 15.11: Addressing mechanisms
Table 15.3:
The IEEE 802.11 frame (wireless LAN) addressing mechanism specifies four cases,
defined by the value of the two flags in the FC field, To DS and From DS.
Each flag can be either 0 or 1, resulting in four different situations.
The interpretation of the four addresses (address 1 to address 4) in the MAC frame depends on the value of these flags, as shown in Table 15.3.

## Slide 12
Figure 15.11: Addressing mechanisms
Table 15.3:
Where distribution is wired, APs are wired, frames between APs are using standard MAC frame 802.3 through distribution system, requires only two addresses (SA and DA)
Rules for addresses:
Address-1, always next device that frame will visit,
Address-2 previous device that frame has left,
Address-3 = Final destination if it is not defined by 1 or original source if not defined by 2, Within Ad hoc, Address-3 = BSS-ID
Address-4-original source when distribution is also wireless, when wired distribution, Address-4= Not applicable (N/A), also same for Ad-hoc
For case-d, address-3 can be destination or original source. Address-4 will be original source (wireless distribution), so address-3 should be final destination

## Slide 13
Addressing mechanisms
Station B is communicating with station F through AP-1 and AP-2 where AP-1 and AP-2 are connected by wired distribution system (LAN)
Addressing:
  Station-B to AP1: Address-1:AP1; address-2: B; Address-3: F, Address-4: not used
Now AP1 will extract information from 802.11 frame and convert it to a 802.3 Frame (Ethernet) and AP1 works as a wireless bridge. Then handover the frame to AP2.
Addressing AP1 to AP2 (Ethernet only two address): Destination address: F and Source address: B
Then AP2 extract information and transforms 802.3 frame to 802.11 frame.
  Addressing AP2 to F: Address-1:F; address-2: AP2; Address-3:B, Address-4: not used
LAN

## Slide 14: Bluetooth
Bluetooth is a form of ad hoc WLAN for interconnecting devices in a very limited area – a Personal Area Network (PAN)
  Useful for connecting telephones, notebooks, computers, cameras, printers, etc.
  Early Bluetooth standardized under IEEE 802.15
  Bluetooth networks are called piconets
    Can have up to eight stations – one primary and up to seven secondaries (active)
    All secondaries are synchronised with primary
    Additional secondaries can exist in the parked state
      Synchronised with primary but cannot participate in communication until it is moved from parked to active state, only 8 stations can be active at a time
    Secondary stations can also be a primary in a second piconet, collectively called a scatternet
      Note: each station can only be a member of two piconets at any one time
    Communication can be one-to-one or one-to-many between primary and secondaries
Notes: Piconet 微微网，多个微微网之间还可以互联形成散射网(Scatternet)

## Slide 15: Bluetooth

## Slide 16: Chapter 16
Other Wireless Networks

## Slide 17: Cellular Telephony
Cellular telephony is designed to provide communications between
  Two moving units or
  One moving unit and one stationary unit
Moving units are known as mobile stations (MSs)
Stationary units are known as land units
Requires:
  Service provider must be able
    to locate and track a caller
    To assign a channel to the call
    To transfer the channel from one base station to another as caller moves

## Slide 18: Cellular Telephony
Each cellular service area is divided into small regions – cells
  Each cell contains an antenna
    Controlled by a solar- or AC-powered network station – a base station
    Base stations controlled by switching office – mobile switching center (MSC)
      MSC coordinates communication between base stations and telephone central office
  Cell size:
    Typically 1-12 miles radius
    Can be increased or decreased depending on population within the cell

## Slide 19: Cellular Telephony
Transmissions within each cell:
  Power kept low to prevent interference with neighbouring cells
  Neighbouring cells generally do not share same set of frequencies to avoid interference for the users near the cell boundaries
    However there is only a limited number of set of frequencies – therefore must be reuse
      A frequency reuse pattern is a configuration of N cells, N is reuse factor, each cell uses a unique set of frequencies
      This is done in a repeating pattern…
      The number in the cells define same pattern
      The cells with same number can use the same set of frequencies
      In N=4, one cell separates the same set of frequencies, in N=7, two cells separate

## Slide 20: Cellular Telephony
To place a call from a mobile station
  Mobile station identifies a channel with a strong signal and contacts the MSC (mobile switching center ) providing the telephone number
  MSC communicates with central office (CO) and assigns unused voice channel to call and establishes connection (if called party available)
To receive a call
  CO communicates with MSC providing telephone number
  MSC searches for location of mobile station by querying each cell – paging
  Once found, MSC sends ringing signal to mobile station
  When answered, MSC assigns voice channel and establishes connection

## Slide 21: Cellular Telephony
MSC monitors the level of signal for each call
  If the signal strength diminishes, MSC seeks a new cell with better reception
  If found, changes call channel (hands off signal from old channel to new)
  Hard Handoff – used in older systems
    Communication broken off with current base station before establishing with new
  Soft Handoff – used in newer systems
    Mobile station can communicate with two base stations simultaneously
    Communication transferred to new base station before breaking off from old
Roaming
  Allows competing networks to provide additional coverage
  Revenue usually shared between providers